## Slide 1: Fundamentals of Business Data Communications 14th Edition Alan Dennis & Alexandra Durcikova John Wiley & Sons, Inc
Dwayne Whitten, D.B.A
Mays Business School
Texas A&M University

## Slide 2: Three Parts to Understanding Networking
Concepts of networking
  How data moves from one computer to another over a network
  Theories of how networks operate
Technologies in use today
  How theories are implemented, specific products
  How do they work, their use, applications
Management of networking technologies
  Security
  Network Design
  Managing the network

## Slide 3: Chapter 1
Introduction to Data Communications

## Slide 4: Chapter 1 Outline
1.1 – Introduction
  Brief history of Data Communications, Communications, Information Systems and the Internet
1.2 - Data Communications Networks
  Network components, network types
1.3 - Network Models
  OSI model, Internet model, transmission via “layers”
1.4 - Network Standards
  Standards making, common standards
1.5 - Future Trends
  Pervasive networking, integration of voice, video, and data, new information services
  1.6 – Implications for Management

## Slide 5: Information Age
First Industrial Revolution
  Introduction of machinery
  New organizational methods
  Changed the way people worked
Second Industrial Revolution – Information Age
  Introduction of computers
  Introduction of networking and data communication
  Changed the way people worked again
    Faster communication  Collapsing Information lag
    Brought people together  Globalization
1.1 Introduction

## Slide 6: The Collapsing Information Lag
1900
1950
2009
1850
large quantities of information transmitted in a fraction of a second
telegraph
Information took days or weeks to be transmitted
Information transmitted in minutes or hours
Historical developments in electronic communications
sped up the rate and volume of transmission of information
growth of telecommunications and especially computer networks
Globalization
of networks
Digitalization

## Slide 7: Advances in Phone Technology
1876
Phone invented
first trans-continental and transatlantic phone connections
1915
1919
Strowger (stepper) switch,
rotary dial phones
(enabling automatic connections)
1948
Microwave trunk lines (Canada)
1962
Telstar (Telecommunications via satellite), Fax services, digital transmission (T-carriers)
1969
Picturefone
(failed commercially)
1976
Packet-switched data communications
1984
Cellular telephone

## Slide 8: Regulation of Inventions
1900
millions of phones in use in the US
Regulation began in the USA (ICC)
1934
FCC established
1968
Carterfone court decision allowing non-Bell CPE
1970
MCI wins court case; begins providing some long distance services
1984
Consent decree by US federal court
1996
1996 US Telecom Act
A time for technological change
1885
AT&T
Phone invented (rapid acceptance)
1876
Bell System:
de facto monopoly
1910
Deregulation
period

## Slide 9: 1984 Consent Decree
Divestiture of 1/1/84: RBOC’s
AT&T broken up into one long distance company (AT&T) and 7 Regional Bell Operating Companies (RBOC’s)
Deregulation: IXC’s and LEC’s
  Competitive long distance (IXC) market; MCI & Sprint enter long distance telephone market (among others)
  Local Exchange Carrier (LEC) service markets remained under RBOC monopoly

## Slide 10: Worldwide Competitive Markets
Internet market
  Extremely competitive with more than 5000 Internet Service Providers (ISPs) in the US alone.
  Heavy competition in this area may lead to a shake out in the near future.
World Trade Organization (WTO) agreement (1997)
  commitments by 68 countries to open, deregulate or lessen regulation in their telecom markets
Multi-national telecom companies
  US companies offering services in Europe, South America
  European companies offering services in USA

## Slide 11: History of Information Systems
Data communications over phone lines (became common and mainframes became multi-user systems)
Batch processing mainframes
Networking everywhere
PC LANs become common
1950
1960
1990
2000
1970
1980
Online real-time, transaction oriented systems (replaced batch processing. DBMSs become common)
PC revolution

## Slide 12: Internet Milestones
Originally called ARPANET, the Internet began as a military-academic network
1969
Worldwide: Over 1 billion Internet users
2007
1990
commercial access to the Internet begins
ARPANET splits:
Milnet - for military
Internet - academic, education and research purposes only
1983
NSFNet created as US Internet backbone
1986
Government funding of the backbone ends
1994

## Slide 13: Net Neutrality
Net neutrality means that for a given type of content (i.e. email,
web, video, etc), all content providers are treated the same.
Net neutrality prevents ISPs from giving priority to some content
providers, while slowing down others

## Slide 14: Thai Telecom
5.4 M Tel Lines
2.3 M Mobile
1994
Thaicom 2
2000
1 Million Internet users
15 ISPs
2007
7 M Tel
51 M Mobile
13 Internet users
2009
1954
TOT Established
1 phone/100 people (TH)
5.6 phone/100 people (BKK)
Mid 1980
1998
1.2 M Internet Hosts
CIA World Factbook
1993
Thaicom 1A Launched
1997
Thaicom 3
2005
Thaicom 4
Thaicom 5
2006
2008
16.1 M Internet Users
Notes: CPE - Customer premise equipments

## Slide 15: 1.2 Data Comm Networks
convergence
Broadband Communications
Telecommunications =
Transmission of voice, video, and/or data
Implies longer distances
- Broad term
Data Communications =
Movement of computer information by means of electrical or optical transmission systems

## Slide 16: Components of a Local Area Network

## Slide 17: Network Types (based on Scale)
Local Area Networks (LAN)
  room, building
  a group of PCs that share a circuit.
Backbone Networks (BN) - less than few kms
  a high speed backbone linking together organizational LANs at various locations.
Wide Area Networks (WANs) - (more than a few kms)
  connects LANs and BNs across different locations
  Often uses leased lines or other services used to transmit data.

## Slide 18: LANs and Backbones, Wide Area and Metropolitan Area Networks

## Slide 19: Intranet vs. Extranet
Intranet
  A LAN that uses the Internet technologies within an organization
  Open only those inside the organization
  Example: insurance related information provided to employees over an intranet
Extranet
  A LAN that uses the Internet technologies across an organization including some external constituents
  Open only those invited users outside the organization
  Accessible through the Internet
  Example: Suppliers and customers accessing inventory information in a company over an extranet

## Slide 20: Layered Implementation of Communications Functions
Applications
OS
Applications
OS
Multi layer implementation
Breaking down into smaller components
Easier to implement
Single layer implementation
-Networking with large components is complex to understand and implement
Applications
OS
Communication
Applications
OS
Communication

## Slide 21: 1.3 Multi-layer Network Models
The two most important such network models: OSI and Internet
Open Systems Interconnection Model
  Created by International Standards Organization (ISO) as a framework for computer network standards in 1984
  Based on 7 layers
Internet Model
  Created by DARPA originally in early 1970’s
  Developed to solve to the problem of internetworking
  Based on 5 layers
  Based on Transmission Control Protocol/ Internet Protocol (TCP/IP) suite

## Slide 22: 7-Layer Model of OSI
Application Layer
  set of utilities used by application programs
Presentation Layer
  formats data for presentation to the user
  provides data interfaces, data compression and translation between different data formats
Session Layer
  initiates, maintains and terminates each logical session between sender and receiver
“Please Do Not Touch Steve’s Pet Alligators”
Physical DataLink Network Transport Session Presentation Application

## Slide 23: 7-Layer Model of OSI
Transport Layer
  deals with end-to-end issues such as segmenting the message for network transport, and maintaining the logical connections between sender and receiver
Network Layer
  responsible for making routing decisions
Data Link Layer
  deals with message delineation, error control and network medium access control
Physical Layer
  defines how individual bits are formatted to be transmitted through the network

## Slide 24: Internet’s 5-Layer Model
Application Layer
  used by application program
Transport Layer
  responsible for establishing end-to-end connections, translates domain names into numeric addresses and segments messages
Network Layer - same as in OSI model
Data Link Layer - same as in OSI model
Physical Layer - same as in OSI model
“Please Do Not Touch Alligators”
Physical DataLink Network Transport Application

## Slide 25: Comparison of Network Models

## Slide 26: Message Transmission Using Layers

## Slide 27: Protocols
Used by network model layers
Sets of standardized rules to define how to communicate at each layer and how to interface with adjacent layers
receiver
sender
Layer N
Layer N-1
Layer N+1
Layer N
Layer N-1
Layer N+1

## Slide 28: Message Transmission Example

## Slide 29: Points about Network Layer View
Layers allow simplicity of networking in some ways
  Easy to develop new software that fits each layer
  Relatively simple to change the software at any level
Matching layers communicate between different computers and computer platforms
  Accomplished by standards that we all agree on
  e.g., Physical layer at the sending computer must match up with the same layer in the receiving computer
Somewhat inefficient
  Involves many software packages and packets
  Packet overhead (slower transmission, processing time)
  Interoperability achieved at the expense of perfectly streamlined communication

## Slide 30: 1.4 Network Standards
Importance
  Provide a “fixed” way for hardware and/or software systems (different companies) to communicate
  Help promote competition and decrease the price
Types of Standards
  The de jure (Formal) standards
    Developed by an industry or government standards-making body
  De-facto standards
    Emerge in the marketplace and widely used
    Lack official backing by a standards-making body

## Slide 31: Standardization Processes
Specification
  Developing the nomenclature and identifying the problems to be addressed
Identification of choices
  Identifying solutions to the problems and choose the “optimum” solution
Acceptance
  Defining the solution, getting it recognized by industry so that a uniform solution is accepted

## Slide 32: Major Standards Bodies
ISO (International Organization for Standardization)
  Technical recommendations for data communication interfaces
  Composed of each country’s national standards orgs.
  Based in Geneva, Switzerland (www.iso.ch)
ITU-T (International Telecommunications Union –Telecom Group
  Technical recommendations about telephone, telegraph and data communications interfaces
  Composed of representatives from each country in UN
  Based in Geneva, Switzerland (www.itu.int)

## Slide 33: Major Standards Bodies (Cont.)
ANSI (American National Standards Institute)
  Coordinating organization for US (not a standards- making body)
  www.ansi.org
IEEE (Institute of Electrical and Electronic Engineers)
  Professional society; also develops mostly LAN standards
  standards.ieee.org
IETF (Internet Engineering Task Force)
  Develops Internet standards
  No official membership (anyone welcome)
  www.ietf.org

## Slide 34: Some Data Comm. Standards
Layer
Common Standards
5. Application layer
HTTP, HTML (Web)
MPEG, H.323 (audio/video)
IMAP, POP (e-mail)
4. Transport layer
TCP (Internet)
SPX (Novell LANs)
3. Network layer
IP (Internet)
IPX (Novell LANs)
2. Data link layer
Ethernet (LAN)
Frame Relay (WAN)
T1 (MAN and WAN)
1. Physical layer
RS-232c cable (LAN)
Category 5 twisted pair (LAN)
V.92 (56 kbps modem)

## Slide 35: 1.5 Current Trends
Wireless LAN and BYOD
Internet of Things
  Pervasive Networking
  Integration of Voice, Video and Data
Massively Online
Cloud Services

## Slide 37
Optimize
Scale
Pioneer
Notes: These trends optimize IT systems for greater reliability, improve data-driven decision making and maintain value and integrity of artificial intelligence (AI) systems in production.
Digital Immune System creates an enhanced customer experience by combining multiple software engineering strategies to protect against risk. Through observability, automation, and extreme design and testing, it delivers resilient systems that mitigate operational and security risks.
Applied Observability works from the data emitted by an organization, using AI to analyze and make recommendations, which allow an enterprise to make faster and more accurate future decisions. When applied systematically, it can reduce the latency for response and optimize business operations in real time.
AI TRiSM AI trust, risk and security management (AI TRiSM) supports AI model governance, trustworthiness, fairness, reliability, robustness, efficacy and data protection. It combines methods for explaining AI results, rapidly deploying new models, actively managing AI security, and controls for privacy and ethics issues.
Theme 2: Scale
These technology trends accelerate vertical offerings, increase the pace of product delivery and enable connectivity everywhere.
Industry Cloud Platforms combine SaaS, PaaS and IaaS with tailored, industry-specific functionality that organizations can use to more easily adapt to the relentless stream of disruptions in their industry.
Platform Engineering provides a curated set of tools, capabilities and processes that are packaged for easy consumption by developers and end users. It will increase end users’ productivity and reduce the burden on development teams.
Wireless-Value Realization covers the provision of wireless network services from everything, including traditional end-user computing, support for edge devices, digital tagging solutions, etc. Such networks go well beyond pure connectivity, providing location and other real-time information and insight from analytics, and allow systems to harvest network energy directly.
Theme 3: Pioneer
These trends focus on enabling business model change, reinventing engagement with employees and customers, and accelerating strategies to tap new virtual markets.
Superapps are more than composite applications that aggregate services. A superapp combines the features of an app, a platform and an ecosystem in one application, providing a platform for third parties to develop and publish their own miniapps on.
Adaptive AI allows for model behavior change post-deployment by using real-time feedback, to continuously retrain models and learn within runtime and development environments, based on new data and adjusted goals, to adapt quickly to changing real-world circumstances.
Metaverse allows people to replicate or enhance their physical activities. This could happen by transporting or extending physical activities to a virtual world or by transforming the physical one. It is a combinatorial innovation made up of multiple technology themes and capabilities.
Theme 4: Sustainable Technology
Delivering technology alone will not be enough in 2023. Sustainable technology is a framework of solutions that increases the energy and efficiency of IT services; enables enterprise sustainability through technologies like traceability, analytics, emissions management software and AI; and helps customers achieve their own sustainability objectives.
Investments in sustainable technology also have the potential to create greater operational resiliency and financial performance, while providing new avenues for growth.

## Slide 40
Notes: A robust digital immune system protects applications and services from anomalies, such as the effects of software bugs or security issues by making applications more resilient so that they recover quickly from failures.
Here are some examples of wireless technologies:
5G: The latest generation of wireless technology, 5G can transmit data at speeds of up to 10 gigabits per second, which is 100 times faster than 4G. Millimeter waves are a promising technology for 5G wireless communications.
Wi-Fi: Wi-Fi can operate on 2.4GHz and 5GHz, with 5GHz being less congested. Wi-Fi has two modes: access point (AP) mode and station mode.
Cellular: Cellular networks provide reliable broadband communication for voice calls and streaming applications.
V2X: V2X technology allows vehicles to communicate with their surroundings, including other vehicles, pedestrians, and infrastructure. This technology is expected to be important for road safety and traffic management in smart cities and with autonomous vehicles.
Satellite: Satellite communication uses satellites orbiting the Earth to transmit and receive signals. It's commonly used for GPS navigation, weather forecasting, and television broadcasting.
Other wireless technologies include: Radio and television broadcasting, Radar communication, Bluetooth, and Radio frequency identification

## Slide 41: 1.6 Implications for Cyber Security
Internet of Things
or
Internet of Targets
Network and Internet change almost everything
  Quickly and easily to move information inside and outside firm
    Easy for cyber criminals to steal info and attack.
      Understand network and Internet is the first step of defense.
Variety of devices connected as BYOD
  Increase the risks as does the IoT
    Secure the computing infrastructure
High demand on network services and capacity
  Secure storage and server space and secure transfer of data
    High Cost on power and staffing
      Cloud can meet or exceed government requirement
IoT

## Slide 42: Ubiquitous
adj. “yoo-bik-wi-tuhs”
Being or seeming to be everywhere at the same time (American Heritage® Dictionary)
Existing or being everywhere at the same time : constantly encountered : widespread (Merriam-Webster Dictionary)